## Slide 1: Robot Locomotion

## Slide 2: Introduction to Robot Locomotion
Robot locomotion refers to how robots move in their environment.
Key systems include mechanical structure, sensors, actuators, and control algorithms.
Main locomotion types: wheeled, legged, tracked, and hybrid.

## Slide 3: Robotics Locomotion Scheme
Defines how a robot generates motion and controls movement.
Includes mobility mechanism, power transmission, and motion control.
Designed based on terrain and task requirements.

## Slide 4: Core Locomotion Concepts
Important factors in locomotion design:
  Stability
  Maneuverability
  Controllability
  Energy efficiency
  Terrain adaptability

## Slide 5: Characteristics of Locomotion
Speed - Maximum travel velocity
Energy consumption - Power needed for motion
Stability - Resistance to tipping
Mechanical complexity - Number of moving components
Terrain capability - Ability to handle obstacles

## Slide 6: Legged Locomotion
Robots move using articulated legs.
Examples - quadrupeds, hexapods, humanoid robots.
Advantages - good for rough terrain.
Disadvantages - high complexity and control requirements.

## Slide 7: Legged Robot Gaits
A gait defines the pattern of leg movement.
Examples - walk, trot, run.
Control algorithms coordinate leg movement and balance.

## Slide 8: Wheeled Locomotion
Most common locomotion type in mobile robotics.
Advantages - simple design, energy efficient, high speed on flat surfaces.
Limitations - poor performance on rough terrain.

## Slide 9: Standard Wheel Configurations
Common wheel configurations
  Differential drive
  Tricycle drive
  Ackermann steering – each wheel turns at different angle
  Omni-directional wheels

## Slide 10: Differential Drive Kinematics
Robot uses two independently driven wheels.
Linear velocity: v = (vR + vL)/2
Angular velocity: ω = (vR − vL)/L
L = distance between wheels.

## Slide 11: Mapping Wheel Rotation to Velocity
Wheel velocity calculation: v = r × ω
  r = wheel radius
  ω = wheel angular velocity
Used to determine robot linear movement.

## Slide 12: Robot Motion on a 2D Plane
Robot pose defined as (x, y, θ).
Motion equations.
dx/dt = v cos θ
dy/dt = v sin θ
dθ/dt = ω

## Slide 13: State Representation
Robot state vector: [x, y, θ].
Used in localization, navigation, and control algorithms.
Sensors estimate robot state during movement.

## Slide 14: Path Planning Overview
Path planning computes route from start to goal avoiding obstacles.
Uses grid maps or graphs.
Key steps - map environment, detect obstacles, compute path.

## Slide 15: A* Path Planning Algorithm
Evaluation function: f(n) = g(n) + h(n)
  g(n): cost from start
  h(n): heuristic estimate to goal
Common heuristic - Manhattan distance.

## Slide 16: Differential Drive Simulation Model
Robot position updated using
  x = x + v cos θ dt
  y = y + v sin θ dt
  θ = θ + ω dt
Used in mobile robot simulators.

## Slide 17: Applications of Robot Locomotion
Autonomous vehicles
Warehouse robots
Delivery robots
Planetary exploration rovers
Service robots

## Slide 18: Programming Mobile Robot Locomotion
Software pipeline:
Sensors → Localization → Path Planning → Motion Control → Motors
Often implemented using Python or C++.

## Slide 19: Summary
Robot locomotion integrates mechanics and control algorithms.
Key topics - wheel kinematics, motion modeling, and path planning.
These concepts enable autonomous mobile robots.

## Slide 20: Locomotion - A Programmer's Perspective
Understanding the Hardware You'll Control

## Slide 21: Welcome – What This Means for You as a Programmer
You're not building motors – you're commanding them
Your Code ──► Commands ──► Hardware ──► Motion ──► Sensors ──► Data ──► Your Code
↑ ↑ ↑ ↑ ↓
What you The "muscle" What What tells Feedback
send you control happens you what loop closes
happened
Understand the hardware well enough to write great control code
Analogy:
  You don't need to build a car engine to drive well
  But you do need to know: gas pedal, brake, steering wheel, and how the car responds

## Slide 22: Motors
In mobile robotics locomotion, PWM (Pulse Width Modulation) and encoders work together to control and measure the motion of DC motors.
PWM controls the motor speed, while the encoder measures the actual rotation of the motor shaft, allowing precise motion control.

## Slide 23: DC Motor in Robotics Locomotion
A DC motor converts electrical energy into rotational motion used to drive.
  Robot wheels
  Robot arms
  Actuators
However, DC motors naturally run at variable speeds depending on voltage and load, so robotics systems must control and monitor them.
Two key components are used.
  PWM → speed control
  Encoder → position and speed measurement

## Slide 24: PWM
PWM is a technique used to control the effective voltage applied to a motor by rapidly switching the power ON and OFF.
Instead of changing voltage directly, the controller changes the duty cycle.
Voltage
5V | ┌───┐ ┌───┐
| │ │ │ │
0V | └───┴───┘ └────
ON OFF
Duty cycle is the percentage of time the signal is ON

## Slide 25: Duty Cycle and motor speed
Duty Cycle | Motor Speed
25% | Slow
50% | Medium
75% | Fast
100% | Maximum
Motor Speed Relation
Supply voltage = 12,
Duty cycle = 50%
Average voltage = 0.5 x 12 = 6 V
The motor behaves roughly as if it received 6 V

## Slide 26: Encoder in Robotics
An encoder measures the rotation of the motor shaft.
Encoders provide feedback for
  speed
  direction
  position
Encoders are essential in closed-loop motor control.

## Slide 27: Types of Encoders
1. Incremental Encoder
Outputs pulses as the shaft rotates
Each pulse = small rotation
2. Quadrature Encoder
Has two signals: Channel A and Channel B, which are phase shifted.
  A: ──▆▆────▆▆────
  B: ─────▆▆────▆▆─
This allows detection of speed and direction

## Slide 28: How PWM and Encoder Work Together
The control system works as a feedback loop.
Controller → PWM → Motor → Wheel
↑ ↓
← Encoder feedback ←
Steps:
Controller sends PWM signal to motor driver
Motor rotates wheel
Encoder produces pulses as shaft rotates
Controller reads encoder pulses
Speed is calculated
PWM is adjusted to reach target speed

## Slide 29: Calculating Motor Speed Using Encoder
Assume, Encoder resolution = 500 pulses per revolution
Measured pulses = 250 pulses in 0.5 seconds
Revolution = 250/500 = 0.5
Resolutions per minute RPM = (0.5/0.5)x60 = 60
60 RPM means the motor shaft makes 60 full turns in one minute.
In robotics, RPM describes how fast the motor shaft or wheel rotates.
E.g 12V DC Motor Speed: 200 RPM

## Slide 30: RPM and Robot Wheel Motion
RPM determines how fast a robot moves.
Relationship between RPM and angular velocity ω=(2π×RPM)/60​
Where, ω = angular velocity (rad/s)
Converting RPM to Robot Linear Velocity
  Robot speed depends on wheel radius.
  v=rω, given r= 0.1m and RPM = 60,
  v= 0.1 x w {w= (2π×RPM)/60 = (2π×60)/60 = 2π
  v=0.1 x 2π = 0.628m/s

## Slide 31: Differential Drive Robot
Robot has
  Left motor + encoder
  Right motor + encoder
Controller performs
  read encoder speed
  compare with desired speed
  adjust PWM
Velocity equations
Linear velocity
  v = (vR + vL)/2
Angular velocity:
ω = (vR − vL)/L
L = wheel separation distance.

## Slide 32
In a differential drive robot,
  Left wheel: 60 RPM, Right wheel: 80 RPM
The robot will turn left because the right wheel moves faster.

## Slide 33: Programming PWM + Encoder Control
target_speed = 100 RPM
while robot_running
  measured_speed = read_encoder()
  error = target_speed - measured_speed
  pwm = pwm + k * error
  set_motor_pwm(pwm)
This is a basic proportional controller.

## Slide 34: Role of PWM + encoder in Robotics Locomotion
PWM + encoder feedback allows robots to
  maintain accurate speed
  perform precise turns
  estimate position (odometry)
  implement autonomous navigation
Used in
  warehouse robots
  delivery robots
  autonomous vehicles

## Slide 35: PWM and encoder
Component | Function
PWM | Controls motor speed
Encoder | Measures motor rotation
Controller | Adjusts PWM using feedback
Together they enable accurate locomotion control in mobile robots.
PWM + encoder systems provide closed-loop motor control in robotics.

## Slide 36: Closed-Loop Motor Control
Closed-loop control means the system continuously measures its output and adjusts the input to achieve a desired result.
For a robot motor:
  Desired value → Target speed or position
  Measured value → Encoder feedback
  Controller → Adjusts PWM signal

## Slide 37: Control loop structure
Target Speed → Controller → PWM → Motor → Wheel
↑ ↓
← Encoder Feedback ←
Steps:
  Controller sets a desired motor speed.
  PWM drives the motor.
  Encoder measures the actual speed.
  Controller calculates the error.
  PWM is adjusted to reduce the error.

## Slide 38: Open-Loop vs Closed-Loop Control
Open-Loop Control
Controller → PWM → Motor
  E.g PWM = 50%
Problem - Motor speed changes with load, friction, or battery voltage.
  E.g No load, motor speed is 100 RPM, but with heavy load, speed reduces to 75RPM
No correction occurs.

## Slide 39: Open-Loop vs Closed-Loop Control
For closed loop
  Target Speed → Controller → Motor ↑ Encoder
E.g Target Speed = 100 RPM, If speed drops to 90 RPM, controller increases PWM.
This ensures consistent motion.
The controller works based on error.
  Error = TargetSpeed − MeasuredSpeed

## Slide 40: PID Control
PID is a control algorithm that adjusts the motor using three components
Term | Meaning
 | Proportional gain
 | Integral gain
 | Derivative gain
e(t) | Error
Term | Meaning
 | Proportional gain
 | Integral gain
 | Derivative gain
e(t) | Error
Output u(t) becomes the PWM signal

## Slide 41: Proportional Control (P)
Control equation.
The proportional term reacts directly to the current error.
P=​ × error
Error = 20 RPM, Kp = 2, p= 20 x 2 = 40
  PWM increpases proportionally
Advantage - Fast response.
Problem - It may leave steady-state error.
Example - Motor stabilizes at 98 RPM instead of 100 RPM.

## Slide 42: Integral Control (I)
Integral control corrects accumulated past errors.
It gradually increases control effort if error persists.
Example: If motor runs at 98 RPM for a long time, integral term pushes it to 100 RPM.
Advantage - Eliminates steady-state error.
Problem - Too much integral gain can cause oscillations.

## Slide 43: Derivative Control (D)
Derivative control predicts future error based on rate of change.
If error changes quickly, derivative term applies braking action.
Example - If motor speed suddenly jumps above target, derivative reduces PWM quickly.
Advantage - Reduces overshoot.
Problem - Sensitive to sensor noise.

## Slide 44: Combined PID Control
Total control signal: PWM=P+I+D
Example: P = 40, I = 10 and D = -5
PWM=45, the Controller sends PWM = 45%.

## Slide 45: Practical Robotics Example PID
Consider a mobile robot wheel motor.
Target speed = 120 RPM, Encoder reading = 100 RPM, error = 120-100 = 20RPM
Controller adjusts PWM
Robot reaches stable speed
Step | Speed | PWM
Start | 100 RPM | 40%
Adjust | 110 RPM | 50%
Stabilize | 120 RPM | 52%

## Slide 46: PID Control Algorithm (Programming)
Example control loop
  error = target_speed - measured_speed
  integral = integral + error * dt
  derivative = (error - previous_error) / dt
  control = Kp*error + Ki*integral + Kd*derivative
  pwm = pwm + control
  previous_error = error
This loop runs many times per second.

## Slide 47: PID in Differential Drive Robots
A robot typically has two motors
  Left Wheel ← PID Controller
  Right Wheel ← PID Controller
Controller ensures both wheels reach target speeds.
Example:
PID corrects both speeds. This ensures straight motion.
Wheel | Target | Actual
Left | 100 RPM | 95 RPM
Right | 100 RPM | 102 RPM

## Slide 48: Benefits of PID in Robotics
PID control enables:
  stable motor speed
  precise motion
  smooth acceleration
  accurate turning
  reliable navigation
Without PID, robots drift or move unpredictably.

## Slide 49: Real Robotics Systems Using PID
PID motor control is used in
  industrial robots
  autonomous vehicles
  drones
  mobile robots
  robotic arms

## Slide 50: Closed-loop motor control
Closed-loop motor control uses feedback from encoders to regulate motor speed.
PID control combines:
  Proportional → reacts to current error
  Integral → corrects past error
  Derivative → predicts future error
Together they allow robots to move accurately and smoothly.

## Slide 51: The Programmer's Mental Model of a Motor
PWM Amplifier (H-Bridge)
YOUR CODE
Forward command
YOUR CODE (AGAIN)
Read encoder, compute next command
ENCODER
Output: Position pulses (A, B phases)
DC MOTOR
Input: Voltage (via PWM)
Output: Torque + Speed
Reverse command
Brake command
In robotics applications, bi-directional control of motor speed is necessary.
This requires a Pulse width modulation (PWM) amplifier to be bipolar, allowing for both forward and backward rotations.
DC motors and PWM amplifiers, are the two most important components involved in a robot power train.
Encoder

## Slide 52: Bipolar PWM amplifier with a built-in cooling fun

## Slide 53: DC Motor
DC servomotor, consisting of a stator, a rotor, and a commutation mechanism
The stator consists of permanent magnets, creating a magnetic field in the air gap between the rotor and the stator.
The rotor has several windings arranged symmetrically around the motor shaft.
As the rotor rotates the polarity of the current flowing to the individual windings is altered. This allows the rotor to rotate continually.

## Slide 54: Reflection
Reflect on the application of motors in driving cars, propellers for a drone and propellers for water vehicle