## Slide 1: The Programmer's Mental Model of a Motor
PWM Amplifier (H-Bridge)
YOUR CODE
Forward command
YOUR CODE (AGAIN)
Read encoder, compute next command
ENCODER
Output: Position pulses (A, B phases)
DC MOTOR
Input: Voltage (via PWM)
Output: Torque + Speed
Reverse command
Brake command
In robotics applications, bi-directional control of motor speed is necessary.
This requires a Pulse width modulation (PWM) amplifier to be bipolar, allowing for both forward and backward rotations.
DC motors and PWM amplifiers, are the two most important components involved in a robot power train.
Encoder

## Slide 2: Path Planning in Robotics
From Geometric Paths to Time‑Optimal Trajectories

## Slide 3: Path Planning in Robotics
Path planning is the process of determining a collision-free route from a start position to a goal position.
Key Idea
  Find where to move (geometry)
  Not necessarily how fast (that’s trajectory planning)
Path - geometric route (no time)
Trajectory - path + timing
Important - planning vs execution

## Slide 4: Path vs Trajectory
Path - geometric route (no time)
Trajectory - path + timing. The position of the robot as a function of time q(t) where q is robot position and t is time
The robot’s position is defined for every moment in time from to (time zero to time final)
Term | Definition | Parameters
Path | Geometric locus of points (no time) | q(s), s∈[0,1]
Trajectory | Path + time + velocity + acceleration | q(t), velocity, acceleration

## Slide 5: Types of Planning
Type | Description
Global Planning | Uses full map knowledge
Local Planning | Reacts to environment in real-time
Static Planning | Environment does not change
Dynamic Planning | Environment changes

## Slide 6: Configuration Space (C-Space)
A robot is represented as a single point in an abstract space.
Key Concepts
  Degree of freedom (DOF) defines dimensions. Each DOF = one dimension
  Obstacles become C-obstacles
In 2-DOF Robot Arm, C=(, ). Instead of planning in physical space → plan in joint space

## Slide 7: Problem (Goal) Formulation
q(s) is a path that describes how the robot moves from start to goal.
Goal - Find q(s) such that:
  Start q(0) = , robot at starting position
  Goal: q(1) = , robot at goal position
Collision-free - q(s) ∉ , robot must not pass through an obstacle.

## Slide 8: Graph-Based Planning
Convert space into a graph - Nodes = positions and Edges = valid paths
Visibility Graph
  Connect all vertices of obstacles; optimal for polygonal obstacles. Produces shortest path. Not safe since the path is too close to obstacles
Voronoi Diagram
  maximizes distance from obstacles. Safe but not shortest
Cell Decomposition
  divide space into regions (simple cells), search adjacency graph
Search: Dijkstra – weighted graph, guarantees shortest path and A* – heuristic‑guided, faster for many problems

## Slide 9: Graph based - Visibility Graph
If you can draw a straight line without hitting an obstacle, connect the points.
Given – start (1,1), goal(9,9), obstacle vertices A(4,4), B (6,4) C(6,6) and D(4,6)
Exercise. Plot the points in a graph and identify the paths between start and goal.
  Identify the shortest path
Use Eucladian distance

## Slide 10: Why Visibility Graph Gives Shortest Path
It connects all straight-line possibilities
The shortest path lies along, straight lines and obstacle edges
Visibility is not save because, visibility graph paths
  pass very close to obstacles
  sometimes touch corners
Risky in real robots due to:
  sensor noise
  control errors

## Slide 11: Graph based - Voronoi Diagram
A Voronoi Diagram divides space such that Every point on a Voronoi edge is equidistant from the nearest obstacles
Move along paths that are as far away from obstacles as possible.
The lines (edges) run between obstacles
These lines form a safe roadmap
Given that Start: S=(1,1), Goal: G=(9,9), Two obstacles: Obstacle 1 at (4,5), Obstacle 2 at (6,5).
Calculate the midpoint between the obstacles x = (4+6)/2 = 5
from Howie Choset

## Slide 12: Graph based - Voronoi Diagram
Given that Start S=(1,1), goal G=(9,9), two obstacles, Obstacle 1 at (4,5), Obstacle 2 at (6,5).
Calculate the midpoint between the obstacles x = (4+6)/2 = 5, which is the Voronoi edge.
Voronoi condition is distance to obstacle 1 and obstacle two are the same.
Constructing the Voronoi Path
Step 1. Build Voronoi edges
  The vertical line x=5 forms a safe corridor
Step 2. Connect Start to Voronoi
From S=(1,1)
  Move toward the nearest Voronoi edge
  Connect to point (5,3) between start S and mid point x=5
Step 3. Follow Voronoi edge
  Move along x=5
Step 4. Connect to Goal
  Leave Voronoi at (5,7)
  Move to G=(9,9)G
The final path is. S→(5,3)→(5,7)→G

## Slide 13: Graph based - Voronoi Algorithm
Add start and goal to the graph
Connect them to nearest Voronoi nodes
Use shortest path search (A*)
Intuition Pick a safe point on the Voronoi line that the robot can reach without hitting obstacles. (5,3) is a convenient, safe connection point chosen on the Voronoi edge, not a fixed formula output.
from Philippe Cheng, MIT, 2001)

## Slide 14: Graph based - Cell Decomposition
Divide the free space into simple regions (cells), then move from one cell to another.
Algorithm
Split space into non-overlapping regions (cells)
Identify which cells are free (no obstacles)
Build a graph of connected cells
Find a path through the cells, Use algorithms like: A*, BFS, Dijkstra.
Convert Cell Path to Real Path. Move from center to center or boundary to boundary

## Slide 15: Dijkstra’s Algorithm
Finds the shortest path from a source node to all other nodes in a weighted graph (weights are non-negative).
  Works only with non-negative edge weights.
  Guarantees the shortest path.
  Uses a greedy approach, always selects the node with the smallest known distance that hasn’t been visited yet.
  Maintains a distance table for the shortest known distance from the source to each node.

## Slide 16: Dijkstra’s Algorithm
Steps
Assign every node a tentative distance value: 0 for the source, ∞ for all others.
Set the source node as current.
For the current node, consider all unvisited neighbors. Calculate tentative distances through the current node.
If the calculated distance is less than the current recorded distance, update it.
Mark the current node as visited (we now know the shortest distance to it).
If there are unvisited nodes left, select the unvisited node with the smallest tentative distance as the new current node.
Repeat steps 3–6 until all nodes are visited.

## Slide 17: Dijkstra’s Algorithm Pseudocode
Algorithm Dijkstra(Graph, source)
Input: Graph with nodes and weighted edges, source node
Output: Shortest distance from source to all other nodes
1. Create a set of unvisited nodes, Unvisited = all nodes in Graph
2. For each node n in Graph
distance[n] = ∞ // tentative distance
previous[n] = undefined // to store the path
3. distance[source] = 0 // distance to itself is 0
4. While Unvisited is not empty
a. current = node in Unvisited with smallest distance
b. For each neighbor n of current that is in Unvisited:
i. alt = distance[current] + weight(current, n)
ii. If alt < distance[n]
distance[n] = alt
previous[n] = current
c. Remove current from Unvisited
5. Return
distance[], previous[]

## Slide 18: A* Algorithm
A* (A-star) is a search algorithm used to find the shortest path from a start point to a goal while avoiding obstacles.
Always move in the direction that looks cheapest AND closest to the goal.
f(n) = g(n) + h(n), where
  g(n) is cost from start → current node
  h(n) is estimated cost from current → goal (heuristic - shortcut that is usually good enough)
  Total estimated cost
A* chooses the node with the smallest f(n)
Heuristic must be admissible
Efficient shortest path search

## Slide 19: How A* Works (Step-by-Step)
Step 1. Initialize
  Put start node in OPEN list
  CLOSED list = empty
Step 2. Repeat
Pick node with lowest f(n)
Move it to CLOSED list
Expand its neighbors
Update costs
Add neighbors to OPEN list
Step 3. Stop
  When the goal node is reached

## Slide 20: Example, Grid-Based Robot
S = Start (0,0), G = Goal (4,4), X = Obstacle
S . . . . . X X . . . . . X . . X . . . . . . . G
h(n) = ∣xgoal​−x∣ + ∣ygoal ​− y∣, called Manhattan distance
Initially, g=0,
  h(n)= (4-0)+(4-0)=8
  f(n) = 0 + 8 = 8
Expand neighbor from (0,0) to (1,0) and (0,1)
Node (1,0), g=1
  h(n)= (4-1)+(4-0)=7
  f(n) = 1 + 7 = 8
Node (1,0), g=1 (moved one step from 0,0 to 0,1
  h(n)= (4-0)+(4-1)=7
  f(n) = 1 + 7 = 8

## Slide 21: Why A* is Powerful
It combines:
  Dijkstra → shortest path
  Greedy search → goal-directed
Heuristic Importance
Good heuristic- speeds up search and gives optimal path
Bad heuristic- slows down and may give wrong path
Condition - h(n)≤true cost, called admissible heuristic

## Slide 22: Programming Structure
open_list = [start]
closed_list = []
while open_list:
current = node_with_lowest_f()
if current == goal:
return path
move current to closed_list
for neighbor in neighbors:
compute g, h, f
update parent
Robotics Applications
A* is used in:
mobile robot navigation
autonomous vehicles
game AI
warehouse robots
Intuition: A* finds the shortest path by balancing cost so far and estimated distance to the goal.

## Slide 23: A* Algorithm
Advantages
Finds optimal path
Efficient with good heuristic
Widely used
Disadvantages
Can be slow in large spaces
Needs good heuristic
High memory usage

## Slide 24: BFS (Breadth-First Search) in Path Planning
Purpose
  BFS is used to find the shortest path in an unweighted graph or grid.
  Guarantees the minimum number of steps (not necessarily the shortest in distance if edges have weights).
  Explores nodes level by level (all nodes at distance 1, then distance 2, etc.).
Key points for robotics
  Grid-based maps are common (cells = nodes).
  Obstacles are blocked cells.
  BFS finds the safest and shortest route in terms of steps.
  Often used in discrete environments.

## Slide 25: Algorithm Steps
Initialize a queue and add the start node.
Mark the start node as visited.
While the queue is not empty a. Remove the front node from the queue (current node). b. For each neighbor of the current node (up, down, left, right in a grid) - If the neighbor is walkable and not visited: - Mark it as visited. - Store its parent (to reconstruct path). - Add it to the queue.
If the goal node is reached, reconstruct the path using the parents.

## Slide 26: Sampling-Based Path Planning
Instead of explicitly modeling all free space, we, sampling based path planning
  Randomly sample configurations
  Keep only collision-free samples
  Connect them to form a graph or tree
  Search for a path
Don’t map everything, just explore enough of the space to find a path
There are two Sampling-Based Methods
  Rapidly-Exploring Random Tree (RRT)
  Probabilistic Roadmap (PRM)

## Slide 27: Rapidly-Exploring Random Trees (RRT)
Grow a tree from the start toward random samples
Steps
Start from qstart
Sample
Find nearest node
Extend toward sample
Add node if safe

## Slide 28: Rapidly-Exploring Random Trees (RRT)
Rapidly-Exploring Random Trees (RRT) are fundamental for motion planning in robotics, especially for high-dimensional systems like robot arms
RRT is a sampling-based path planning algorithm that builds a tree by:
  Randomly sampling points in space
  Connecting them to the nearest existing node
  Growing toward unexplored regions

## Slide 29: Rapidly-Exploring Random Trees RRT
Grow a tree from the start by randomly exploring the space until you reach the goal.
RRT algorithm is a single-query method that quickly generates a route by finding the destination while expanding the roadmap from the starting point.

## Slide 32: Sampling-Based Planning (RRT)
Rapidly‑exploring Random Tree (RRT)
Grow a tree by randomly sampling configurations and extending toward them.
Properties
  Probabilistically complete
  Random sampling + tree expansion
  Variants: RRT*, Informed RRT for optimality
Good for high-dimensional spaces

## Slide 33: RRT Algorithm
Every node is connected to another node called a “parent”, and the start point becomes the root.
A sample node (𝑞𝑟𝑎𝑛𝑑) is generated, and the closest node (𝑞𝑛𝑒𝑎𝑟) from 𝑞𝑟𝑎𝑛𝑑 is found in the tree (a).
A node separated by distance (𝑟) on a straight line connected from 𝑞𝑛𝑒𝑎𝑟 to 𝑞𝑟𝑎𝑛𝑑 is generated as a new node (𝑞𝑛𝑒𝑤) (b).
𝑞𝑛𝑒𝑤 is then added to the tree if a straight line from 𝑞𝑛𝑒𝑎𝑟 to 𝑞𝑛𝑒𝑤 does not collide with an obstacle.
This process is repeated (c). If the straight line from 𝑞𝑛𝑒𝑎𝑟 to qnew collides with an obstacle in the tree-expanding step, the existing node 𝑞𝑟𝑎𝑛𝑑 is discarded (d), and a new node 𝑞𝑟𝑎𝑛𝑑 is generated.
The tree generation process is then repeated (e).

## Slide 34
RRT Algorithm

## Slide 35: RRT Algorithm
a) Select a 𝑞𝑟𝑎𝑛𝑑 and 𝑞𝑛𝑒𝑎𝑟,
(b) select a 𝑞𝑛𝑒𝑎𝑟 within distance 𝑟,
(c) repeat ‘(a) and (b)’ process, (d) if collision occurs regenerate 𝑞𝑟𝑎𝑛𝑑,
(e) regenerate 𝑞𝑟𝑎𝑛𝑑 without collision, and
(f) repeat process to 𝑞𝑔𝑜𝑎𝑙.
Jang, D.-u., & Kim, J.-s. (2022). Development of Ship Route-Planning Algorithm Based on Rapidly-Exploring Random Tree (RRT*) Using Designated Space. Journal of Marine Science and Engineering, 10(12), 1800. https://doi.org/10.3390/jmse10121800

## Slide 36: Rapidly‑exploring Random Tree (RRT) Algorithm
RRT(start, goal, max_iter):
tree = {start}
for i in 1..max_iter:
q_rand = sample_configuration()
q_near = nearest_neighbor(tree, q_rand)
q_new = steer(q_near, q_rand, step_size)
if collision_free(q_near, q_new):
tree.add(q_new)
if distance(q_new, goal) < threshold:
return path
  reurn failure

## Slide 37: The Probabilistic Road Map (PRM)
Build a network (roadmap) of random points, then search through it
Steps
Sample random points in free space
Keep collision-free points
Connect nearby points
Build a graph
Use A* or Dijkstra to find path

## Slide 38: The Probabilistic Road Map (PRM)
The PRM is a network graph of the possible routes in each map based on free and occupied spaces.
First, the nodes are randomly generated in a space with obstacles (a).
Whether a node is in free space is checked using the multiple-query method, after which it is connected to the closest node at a certain distance (b)
Whether the edge that interconnects the nodes crosses an obstacle can then be determined (c)
The roadmap is generated by repeating this
Process until all samples are passed and the optimal route is found (d)

## Slide 39
PRM algorithm

## Slide 40: PRM
Two‑phase method
Construction phase
  Randomly sample collision‑free configurations
  Connect nearby samples with collision‑free local paths
Query phase
  Connect start/goal to graph
  Search for shortest path
Advantages
  Precomputation for multiple queries
  Works well in static environments
  Trade‑off: Less efficient for single queries than RRT.

## Slide 41: PRM
The learning process of typical PRM algorithm: (a) Obtaining free points; and (b) constructing collision-free line segments.

## Slide 42: Probabilistic Roadmaps (PRM)
Advantages
  Good for repeated queries
  Efficient once roadmap is built
Disadvantages
  Slow initial construction
  Not ideal for single query