## Slide 1: Trajectory

## Slide 2: Path Planning in Robotics
Path planning is the process of determining a collision-free route from a start position to a goal position.
Key Idea
  Find where to move (geometry)
  Not necessarily how fast (that’s trajectory planning)
Path - geometric route (no time)
Trajectory - path + timing
Important - planning vs execution

## Slide 3: Path vs Trajectory
Path - geometric route (no time)
Trajectory - path + timing. The position of the robot as a function of time q(t) where q is robot position and t is time
The robot’s position is defined for every moment in time from to (time zero to time final)
Term | Definition | Parameters
Path | Geometric locus of points (no time) | q(s), s∈[0,1]
Trajectory | Path + time + velocity + acceleration | q(t), velocity, acceleration

## Slide 4: Trajectory
A trajectory describes how a robot moves over time.
Trajectory; path + timing. The position of the robot as a function of time q(t) where q is robot position or joint angle and t is time
The robot’s position is defined for every moment in time from to (time zero to time final)

## Slide 5: Joint vs Cartesian Space
Joint space
  Path in 𝒞‑space: q(t)
  No Inverse Kinematics needed, smooth joint motion
  End‑effector motion unpredictable
Cartesian Space
  intuitive motion
  Path in workspace x(t), orientation
  Intuitive for tasks requiring specific tool paths
  Inverse Kinematics at each step, singularities

## Slide 6: Types of trajectory
Joint Space Trajectory
  Plan motion in joint angles
  q(t) = [θ1 (t), θ2(t), … ]
  Used in robot arms
Cartesian Space Trajectory
  Plan motion in task space
  x(t), y(t), z(t)
  Requires inverse kinematics

## Slide 7: Trajectory Requirements
A good trajectory must
Start and end at correct positions
Be smooth
Respect velocity & acceleration limits
Avoid sudden jerks

## Slide 8: Polynomial Trajectories - Cubic Trajectory
A cubic trajectory defines robot motion using a 3rd-degree polynomial that defines position as a function of time.
Ensures smooth velocity
  It allows us to specify position and velocity at both start and end points, ensuring smooth motion without velocity jumps.
Used for basic motion
Boundary Conditions, We specify:
  Initial position , Final position
  Initial velocity , Final velocity

## Slide 9: Cubic Trajectory
Once we have the polynomial coefficients, we differentiate to obtain velocity and acceleration
Equation
Velocity
Acceleration
Solving for Coefficients

## Slide 10: Cubic Trajectory - Solving for Coefficients
Coefficients
Step 1: At t=0
Step 2: At t=

## Slide 11: Cubic Trajectory - Solving for Coefficients
Coefficients
Step 3: Solve for

## Slide 12: Worked example
Given:
Start: = 0
End: = 10
Initial velocity: = 0
Final velocity: = 0
Time: = 2
Step 1: Compute coefficients
  = 0, =0
Compute a2
Compute a3
Step 2: Final Equation (degrees)
Check q(t) when t = 0, 2

## Slide 13: Quintic Trajectories in Robotics
A quintic trajectory is a 5th-degree polynomial used in motion planning to generate smooth paths for robotic systems.
It has the general form: q(t) = a0 + a1t + a2t2 + a3t3 + a4t4 + a5 t5 Where:
  q(t): position
  q˙(t) : velocity
  q¨(t): acceleration
  a0 … a5 ​: coefficients determined by boundary conditions

## Slide 14: Why Quintic Trajectories?
Quintic polynomials are preferred because they allow control over:
  Position
  Velocity
  Acceleration
at both the start and end points of motion.
This gives 6 boundary conditions, matching the 6 coefficients.
Ensures smooth motion.

## Slide 15: Boundary Conditions
For a motion from time t= 0 to t=T, we define:
At t = 0:
  q(0) = q0 position
  q˙(0) =v0 velocity - change in position over time
  q¨(0) =a0 Acceleration - change in velocity over time
At t=T:
  q(T)=qf ​
  q˙(T)=vf
  q¨(T)=af
These constraints ensure smooth start and stop.

## Slide 16: Acceleration constraints
Acceleration constraints are critical because
  High acceleration can damage actuators
  Causes mechanical stress
  Reduces system lifespan
Acceleration is the second derivative
  q¨​(t )= 2a2​ + 6a3​t + 12a4​t2 + 20a5​t3
Key properties
  Acceleration is continuous
  Can be constrained at endpoints
  Avoids sudden jumps (unlike cubic trajectories)
Practical Constraint Handling
  Set a0​ = 0 and af =0 for smooth rest-to-rest motion
Limit peak acceleration using
  Time scaling (increase T)
  Optimization-based trajectory generation

## Slide 17: Jerk Control
Jerk is the rate of change of acceleration, Jerk = d3q / dt3
For quintic trajectories, q′′′(t) = 6a3​ + 24a4​t + 60a5​t2
Why Jerk Control Matters
  Reduces vibration
  Prevents oscillations
  Improves tracking accuracy
  Enhances user safety (especially in human-robot interaction)

## Slide 18: Comparison
Advantages of Quintic Trajectories
  Continuous jerk profile
  No abrupt acceleration changes
  Smooth transition between motion phases
Comparison
  Cubic: Discontinuous acceleration
  Quintic: Smooth acceleration and jerk
Trajectory Type | Position | Velocity | Acceleration | Jerk
Cubic | Smooth | Smooth | Discontinuous | Infinite spikes
Quintic | Smooth | Smooth | Smooth | Continuous

## Slide 19: Applications
Industrial robots
Medical robots
Autonomous vehicles
Semiconductor systems
CNC machines - Computer Numerical Control machines in robotics are automated manufacturing systems that use programmed instructions to control tools and machinery with high precision.

## Slide 20: Applications
Quintic trajectories are widely used in high-precision systems
a) Industrial Robotics - Robotic arms (e.g., assembly lines), Welding and painting robots
  Ensures smooth tool motion and high accuracy
b) Medical Robotics - Surgical robots, Prosthetics and rehabilitation devices
  Requires extremely smooth motion to avoid harm
c) CNC Machines - Tool path planning
  Minimizes vibration and improves surface finish
d) Autonomous Systems Drones and self-driving vehicles
  Smooth navigation and passenger comfort
e) Semiconductor Manufacturing Ultra-precise positioning systems
  Nanometer-level accuracy requirements

## Slide 21: Advantages and limitations
Key Advantages
Smooth position, velocity, and acceleration profiles
Reduced mechanical wear and tear
Improved control stability
Better tracking performance
Ideal for high-speed, high-precision tasks
Limitations
Computationally more complex than lower-order polynomials
May require optimization for strict constraints
Not always sufficient for highly dynamic environments (may need spline-based or jerk-limited profiles)

## Slide 22: Quintic trajectories
Quintic trajectories are a powerful tool in robotic motion planning, especially where
  Smoothness is critical
  Acceleration and jerk must be controlled
  Precision and safety are required
They strike a balance between mathematical simplicity and physical realism, making them a standard choice in modern robotics.
Quintic trajectories are ideal for precision robotics requiring smooth, safe, and accurate motion.

## Slide 23: Linear Segment with Parabolic Blend (LSPB) Trajectory
Idea
  Accelerate
  Move at constant speed
  Decelerate
Velocity Profile
  Start → acceleration
  Middle → constant velocity
  End → deceleration
Trapezoidal velocity
Phases - accel, constant, decel
Efficient and simple

## Slide 24: Example - LSPB Trajectory
Given:
  Distance = 10 m
  Max velocity = 4 m/s
  Acceleration = 2 m/s²
Step 1: Time to accelerate ta=v/a = 4/2 = 2 s
Step 2: Distance during acceleration da​=1/2(​at2) = 4
Step 3: Remaining distance 10−2(4) = 2
Step 4: Constant velocity time tc​ = 2/4 ​=0.5 s
Total time T = 2 + 0.5 + 2 = 4.5 s
Total motion time = time to speed up + time at full speed + time to slow down
The Three Phases
1. Acceleration Phase
  t1 ​ = 2 s
  Robot speeds up from 0 to max velocity
  Motion is accelerating
2. Constant Velocity Phase
  t2 ​= 0.5 s
  Robot moves at maximum speed
  No acceleration
3. Deceleration Phase
  t3​ = 2 s
  Robot slows down to stop
  Motion is decelerating
https://www.mathworks.com/help/robotics/ug/design-a-trajectory-with-velocity-limits-using-a-trapezoidal-velocity-profile.html?utm_source=chatgpt.com

## Slide 25: Multi-Point Trajectory (Spline)
Idea - Pass through multiple points smoothly q0 ​→ q1 ​→ q2​ → q3​
Use - Cubic splines, B-splines
Ensures smooth motion

## Slide 26: S-Curve Profile
Limits jerk
Smooth transitions
Used in high precision systems

## Slide 27: Cubic Spline Example
In robotics, we often want a robot to move through multiple points:
  q0 ​→ q1 ​→ q2​ → q3​
A single polynomial is NOT enough because:
  it becomes unstable
  it cannot maintain smoothness across many points
Solution: Splines
Key Idea: “Break the motion into smaller smooth pieces and join them together.”

## Slide 28: Cubic spline
A cubic spline is a set of piecewise cubic polynomials, one between each pair of points.
For points: q0​, q1​, q2​, q3​
We define:
  Segment 1: between q0→q1
  Segment 2: between q1→q2 ​
  Segment 3: between q2→q3 ​
Each segment: qi(t) = ai + bit + cit2 + dit3

## Slide 29: Conditions for cubic spline
At each connecting point:
  Position must match
  Velocity must match
  Acceleration must match
This ensures
  Smooth motion
  No jerks
  Continuous acceleration

## Slide 30: Conditions for cubic spline
Given Points
  q0 ​= 0, q1​ = 5, q2 ​= 8, q3​ = 10
What happens?
  Robot moves from 0 → 5 smoothly
  Then 5 → 8 smoothly
  Then 8 → 10 smoothly
No sharp turns or stops
Why Cubic Splines Are Good
  Smooth motion
  Passes exactly through all points
  Easy to compute
Limitation
  Changing one point affects the whole curve

## Slide 31: B-Splines (Basis Splines)
A B-spline is a smooth curve controlled by control points, but:
  It does NOT necessarily pass through all points
Key Idea : “Control the shape of the curve using nearby points instead of forcing it through every point.”
Instead of interpolation:
  q(t) = ∑ Bi​(t)Pi​
Where:
  Pi​ = control points
  Bi(t) = basis functions

## Slide 32: Example (B-Spline)
Control Points:
  P0 = (-1,0), P1 = (-3,3), P2 = (4,1), P3 = (2,1) p4 = (1,3)
The curve:
  does NOT pass through all points
  stays close to them
  forms a smooth path
Key Property - Local Control
If you move one control point
  Only part of the curve changes
  Not the entire curve

## Slide 33: Cubic Spline vs B-Spline
Feature | Cubic Spline | B-Spline
Passes through points | Yes | No
Smoothness | High | Very high
Control | Global | Local
Stability | Moderate | Very stable
Use Cubic Splines when
Robot must pass through exact points
Waypoints are critical
Use B-Splines when
Smoothness is more important
You want flexible shape control
Avoid sharp changes

## Slide 34: Robotics Application
Cubic Splines
  Industrial robot arms
  Pick-and-place tasks
“Go exactly through every point smoothly.”
Cubic spline → interpolates points
B-Splines
  Autonomous vehicles
  Drone flight paths
  Animation and smooth navigation
Follow the general direction of points with maximum smoothness.”
B-spline → approximates points
Both ensure smooth trajectories

## Slide 35: Trajectory Architecture (planning pipeline)
Planner → Generator → Controller
Ensures smooth execution
Path planning
Time assignment
Trajectory generation
Control execution

## Slide 36: Applications of trajectory
Trajectory planning is used in:
  robotic arms
  mobile robots
  drones
  autonomous vehicles
Frameworks like: ROS MoveIt
  Motion planning framework
  Uses RRT/PRM
  Handles Inverse Kinematics and trajectories
Trajectory planning tells the robot not just where to go, but how fast and how smoothly to get there.
Always remember
q(t) defines motion
Cubic → position + velocity
Quintic → position + velocity + acceleration
LSPB → practical velocity profile

## Slide 37: Obstacle Avoidance
Obstacle avoidance
Ensures that a robot:
  Moves from start → goal
  Without colliding with obstacles
Key Idea - “Every motion must be checked for safety before execution.”
Configuration Space (C-Space)
Instead of thinking about the robot in physical space
  Represent robot as a point in configuration space
Example
  A 2D robot → position (x, y)
  A robotic arm → joint angles (θ1​, θ2​, …)
Important
  Obstacles become C-obstacles
  Free space = valid region

## Slide 38: Collision Checking
Determines Whether a robot configuration or motion is collision-free
Types of Collision Checking
1. Point Collision Check
  Check a single configuration: q = (x, y)
  Is it inside obstacle? → ❌ collision
  Outside? → ✅ safe
2. Path Collision Check
Check motion between two points: q1 ​→ q2
Method:
  Divide path into small segments
  Check each segment
Algorithms Used
Bounding boxes
Mesh intersection
Distance threshold methods

## Slide 39: Distance Fields
A distance field assigns the distance from each point to the nearest obstacle
Mathematical Form d(x, y) = distance to nearest obstacle
Types
1. Unsigned Distance Field
  Only gives distance
  Always positive
2. Signed Distance Field (SDF) d(x) = {+outside obstacle−inside obstacle​}
Why Distance Fields Are Useful
They provide:
Clearance information
  Smooth gradients
  Safer paths
Example : Obstacle at center:
  Point near obstacle → distance = small
  Far point → distance = large
Use in Safety - Robot should maintain d(x) > dsafe

## Slide 40: Distance Fields in Motion Planning
Use Cases
  Collision checking
  Path optimization
  Gradient-based planning
Example - Robot prefers path:
  Far from obstacles
  Smooth

## Slide 41: Use in PRM (Probabilistic Roadmap)
How PRM Uses Collision Checking
  Sample random points
  Keep only collision-free points
  Connect nodes if path is collision-free
With Distance Fields
  Prefer nodes with large clearance
  Avoid narrow passages
Example
  Two nodes connected only if safe path exists
  Distance field ensures safer connections

## Slide 42: Use in RRT (Rapidly-Exploring Random Tree)
How RRT Uses Collision Checking
  Every step: qnear ​→ qnew​
  Must be checked for collision
With Distance Fields
  Guide tree growth away from obstacles
  Improve safety
Example - Instead of random growth, bias toward safe regions

## Slide 43: Key Insights
Collision checking = YES/NO decision
Distance field = HOW SAFE decision
RRT & PRM rely heavily on:
  fast collision detection
  efficient distance computation
Intuition - “Collision checking prevents crashes, distance fields keep the robot safely away from danger.”
Facts
  Collision checking → verifies path validity
  Distance field → measures clearance
  Used in RRT/PRM for safe planning

## Slide 44: Summary
Path → where
Trajectory → how fast
Combined for real robot motion

## Slide 45: Further Reading
Siciliano Robotics
LaValle Planning Algorithms
OMPL, MoveIt, PyBullet
Understanding planning is mastering robotics motion

## Slide 46: Reflection questions
1. Conceptual Understanding & Distinction
  How would you clearly distinguish between path planning and trajectory generation in a real robotic system? Can a robot operate effectively using only one of them? Why or why not?
  Why is it insufficient to treat a planned path as directly executable by a robot without trajectory considerations?
  In what situations might a “shortest path” be a poor choice for robot navigation?
2. Representation of the Environment
  What are the trade-offs between grid-based, graph-based, and continuous representations in path planning?
  How does the choice of environment representation affect computational efficiency and optimality of the solution?
  In dynamic environments, what limitations arise from static map-based planning methods?
3. Algorithmic Reasoning
  Dijkstra’s algorithm guarantees optimality—why is it still not always preferred in real-time robotic applications?
  How does A* improve upon Dijkstra’s algorithm, and under what conditions does it degrade to Dijkstra’s behavior?
  What are the advantages and weaknesses of sampling-based methods like RRT and PRM in high-dimensional spaces?
4. Constraints and Real-World Feasibility
  Why must trajectory planning consider velocity, acceleration, and jerk constraints even if the path is collision-free?
  What could go wrong if a robot follows a path that violates its dynamic constraints?
  How do physical constraints of different robots (e.g., drones vs wheeled robots) influence trajectory design?

## Slide 47: Reflection questions
5. Optimization and Trade-offs
  Is the “shortest path” always the “best path”? What other cost functions might be more realistic?
  How do we balance computational efficiency vs optimality in real-time path planning systems?
  When would you prefer a suboptimal but fast solution over an optimal but slow solution?
6. Uncertainty and Robustness
  How should path planning algorithms account for uncertainty in sensor data and environmental perception?
  What are the risks of assuming perfect map knowledge in real-world navigation?
  How can probabilistic approaches improve robustness in uncertain environments?
7. Dynamic and Real-Time Planning
  Why is re-planning necessary in dynamic environments, and what are the computational challenges involved?
  How do local planners complement global planners in autonomous navigation systems?
  Can a purely global planner work effectively in real-time obstacle-rich environments? Defend your answer.

## Slide 48: Reflection questions
8. Trajectory Smoothness and Control
  Why is jerk minimization important in trajectory generation for precision robotics?
  How does trajectory smoothness affect mechanical wear and energy efficiency?
  What are the consequences of abrupt changes in velocity or acceleration in robotic motion?
9. Comparative Thinking
  Compare grid-based planning vs sampling-based planning in terms of scalability and accuracy.
  Compare deterministic vs probabilistic path planning approaches. Which is more suitable for unknown environments and why?
  How do classical planning methods compare with learning-based approaches in modern robotics?
10. Design and Synthesis Questions
  Design a path planning system for a warehouse robot that must avoid humans, optimize delivery time, and minimize energy use. What components would you include?
  If you were to design a planner for a self-driving car in Kampala traffic conditions, what key challenges would you prioritize?
  Propose an improvement to RRT that could make it more suitable for real-time autonomous drone navigation.