## Slide 1: Perception and sensing

## Slide 2: Perception in Robotics
Perception in robotics is the process by which a robot
  Acquires raw data from sensors
  Processes and interprets that data
  Builds a meaningful representation of the environment
It transforms sensor data into knowledge about the world (environment).
Perception converts sensor signals into state estimates (e.g., position, obstacles, objects).
The algorithmic interpretation of that sensor data into a representation the robot can reason about and act upon.
perception is about sense – plan – act pipeline, where sensing data is processed into a representation used for decision-making .
A robot vacuum uses
  Sensors → detect walls and obstacles
  Perception → interprets distances and shapes
  Output → “There is a wall ahead”
Perception = Sensing + Interpretation + State Estimation
Perception is not about truth; it is about building a Belief State.
  Due to sensor noise and environmental ambiguity, the robot maintains a probabilistic belief (e.g., "I am 95% certain this is a door and 5% otherwise").

## Slide 3: The Perception Challenge
Why is Perception Difficult?
1. Uncertainty and Noise
  Sensors produce imperfect data
  E.g A camera may misinterpret shadows as obstacles
2. Partial Observability
  Robots cannot see everything e.g Objects hidden behind walls
3. Dynamic Environments
  Environment changes constantly e.g moving cars, people
4. High Dimensional Data
  Sensors like cameras generate massive data
  Requires real-time processing
5. Ambiguity
  Same sensor data can have multiple interpretations e.g Is that a rock or a shadow?
6. Sensor Limitations
Each sensor has weaknesses:
  Camera → affected by lighting
  LiDAR → expensive
  Ultrasonic → low resolution
Perception is not just sensing, it involves reasoning under uncertainty.

## Slide 4: The Perception Challenge
Challenge Category | Description | Concrete Example
Noise & Uncertainty | All sensors are corrupted by random statistical error. | A LIDAR beam hitting a glass window. Some photons pass through, some reflect. The distance reading becomes erratic or "infinite."
Ambiguity | The same sensor data can correspond to multiple world states. | A Camera sees a dark rectangular shape on the floor. Is it a hole (danger), a shadow (safe), or a stain (safe)? Vision alone cannot disambiguate this reliably.
Dimensionality | Sensors produce massive data streams (e.g., 2D images, 3D point clouds). | A standard HD Camera produces ~30 MB of raw data per second. A robot must process this in real-time on embedded hardware with limited power.
Dynamic Range & Environment | Lighting, weather, and texture vary wildly. | SLAM (Simultaneous Localization and Mapping) works perfectly indoors but fails in a featureless cornfield or a foggy construction site where LIDAR beams scatter.

## Slide 5: Mobile Robot Control System Architecture
The Sense – Plan – Act (SPA) architecture is the classical framework for robot control.
The SPA Loop
Robots operate in a continuous loop:
  Sense → collect data from sensor. Process data into a World Model (Map + Localization).
  Plan → decide what to do. Use the World Model to compute a path or trajectory from current state to goal state (e.g., A* algorithm, RRT).
  Act → execute actions. Send low-level commands (velocity, steering angle) to the Actuators (motors).
This cycle repeats continuously .
1. Sense Layer (Perception Stage)
Collects data from sensors
Processes it into meaningful information. E.g.
  Camera detects a pedestrian
  LiDAR measures distance
2. Plan Layer
Builds a world model, decides next action e.g.
  “Obstacle ahead → turn left”
3. Act Layer
Executes commands via actuators e.g. Motors rotate wheels

## Slide 6: Sense – Plan – Act (SPA)
Real-Life Example (Self-driving car)
  Sense → detect traffic lights
  Plan → decide to stop
  Act → apply brakes
Limitations of SPA
Slow in dynamic environments
  Pure SPA is open-loop within each cycle. If the environment changes while the robot is moving between Sense and Act, the robot will execute a plan based on stale data.
Heavy reliance on accurate world models
Sequential processing can delay response

## Slide 7: Evolution of Robotic Control Architectures
1. Classical (Deliberative) Architecture
Based on SPA
Uses global world model
  Strength: Accurate planning
  Weakness: Slow, not reactive
2. Reactive Architecture
Direct mapping: Sense → Act (no planning)
E.g. Obstacle detected → immediately turn
  Strength: Fast response
  Weakness: No long-term planning
3. Hybrid Architecture
Combines:
  Planning (deliberative)
  Reaction (real-time)
Most modern robots use this approach
Deliberative Layer (SPA):
  Slow, smart, global. Runs at 1-10 Hz. Uses heavy perception (object detection, global map update).
Reactive Layer (Sense-Act):
  Fast, dumb, local. Runs at 100-1000 Hz. Uses direct sensor feedback (e.g., "If LIDAR front distance < 0.5m, STOP").

## Slide 8: Classification of Robotic Sensors
Sensors are the foundation of perception.
A. Proprioceptive Sensors (Internal)
Sensors that measure the internal state of the robot e.g.
  Joint angle sensors
  Wheel encoders
  Gyroscopes
  Accelerometers
Function - tell the robot
  “Where am I?”
  “How fast am I moving?”
E.g. a robotic arm uses encoders to know joint angles
B. Exteroceptive Sensors (External)
Sensors that measure the external environment e.g.
  Cameras (vision)
  LiDAR (distance mapping)
  Ultrasonic sensors
  GPS
  Infrared sensors
Function - tell the robot:
  “What is around me?”
E.g. a drone uses GPS + camera to navigate

## Slide 9: Comparison of Sensor Types
Property | Proprioceptive Sensors (Internal State) | Exteroceptive Sensors (External World)
What they measure | Internal state Quantities within the robot's own body. | External environment Quantities outside the robot relative to the environment.
Examples | Encoders, IMU | Camera, LiDAR
Accuracy | Usually high | Often noisy
Role | Self-awareness | Environmental awareness
Drift Behavior | Drifts over time (errors accumulate). | No Drift (errors are bounded per reading).
Environmental Dependency | Unaffected by weather or lighting. | Affected by weather, lighting, and structure.
Analogy | Closing your eyes and counting steps. | Opening your eyes to look at landmarks.

## Slide 10: Proprioceptive Sensors (The Inner Ear & Muscle Sense)
Sensor Type | Principle | Output | Example Use Case
Incremental Encoder | Counts ticks/notches on a spinning motor shaft. | Wheel Revolutions -> Odometry (Position Estimate). | Example: "I turned left wheel 500 ticks, right wheel 505 ticks. Therefore, I have moved forward 10cm." (Drifts ~5-10% per meter traveled).
Inertial Measurement Unit (IMU) | Combines Accelerometer (linear force) + Gyroscope (angular rate). | Roll, Pitch, Yaw (Orientation). | Example: A drone must have an IMU. It senses it is tilting 15 degrees right and corrects the motor thrust before the camera even sees the horizon moving.
Motor Current Sensor | Measures Amps drawn by motor. | Torque Estimation / Collision Detection. | Example: A collaborative robot arm ("Cobot"). If current spikes unexpectedly without a command to accelerate, the robot knows it hit a human and stops in <10ms.

## Slide 11: Exteroceptive Sensors (The Eyes and Ears)
Sensor Type | Principle | Output | Example Use Case
Time-of-Flight (ToF) LIDAR | Emits laser pulse, measures time for light to return. | Point Cloud (3D distance map). | Waymo's "Laser Bear". Creates a 360-degree, centimeter-accurate model of cars and curbs, even in pitch-black night.
Monocular Camera | Captures 2D projection of 3D world via CMOS sensor. | RGB Image (Semantic Info). | Tesla Vision. Identifies a "Yellow Traffic Light" state. Challenge: Monocular cameras inherently lack Scale. A small car close looks identical to a big car far away.
Stereo Camera | Two lenses, known baseline distance. Uses Disparity (triangulation). | RGB-Depth Image (Dense). | Boston Dynamics Spot. Navigates stairs by matching features in left/right eye to calculate precise step height. Limitation: Fails in textureless white walls or darkness.
RADAR | Emits radio waves, measures Doppler Shift (frequency change). | Position AND Instantaneous Velocity. | Adaptive Cruise Control. A camera might confuse a shadow for a car braking. RADAR directly measures the closing speed of the metal object ahead with 99.9% certainty in a blizzard.

## Slide 12: Historical Evolution
Era | Dominant Sensors | Limitation
Dead Reckoning Era (1970s-80s) | Wheel Encoders, Compasses | Drift accumulation. Shakey the Robot got lost in corners.
Sonar Era (1980s-90s) | Ultrasonic Range Finders | Specular reflection (sound bounces off smooth walls at an angle, reporting false long distances).
LIDAR Era (2000s-2015s) | 2D Scanning Laser Rangefinders (SICK, Hokuyo) | The "Gold Standard" for planar mapping (e.g., Roomba high-end models). Expensive and blind to glass.
Visual Era (2015s-Present) | Monocular & Stereo Cameras, RGB-D | Driven by deep learning. Rich semantic data but computationally heavy and poor in low-light.
Sensor Fusion Era (Current) | IMU + Camera + LIDAR + Radar | Redundancy. Use Radar for velocity in fog, Camera for sign reading, LIDAR for precise shape.

## Slide 13: Sensor Fusion
Combining data from multiple sensors to improve perception
Why Needed?
  No single sensor is perfect
E.g Self-driving car
  Camera → detects objects
  LiDAR → measures distance
  Radar → detects speed
Practical Applications
Autonomous Vehicles
  Use cameras, radar, LiDAR
  Perform real-time perception and decision-making
Industrial Robots
  Use force sensors and encoders for precision
Drones
  Use IMU + GPS + vision for navigation

## Slide 14: Choosing the Right Sensor
If you need... | Best Choice | Why
Long Range in Fog/Rain | RADAR | Radio waves penetrate water droplets.
Precise 3D Shape at Night | LIDAR | Active illumination, high angular resolution.
Read a Street Sign | Camera | Only passive visual li ght carries this semantic info.
Know if the Floor is Slipping | IMU + Wheel Encoder | Compare expected motion (Encoders) to actual motion (IMU). Discrepancy = Slip.
Fast, Cheap Obstacle Stop | Ultrasonic (Sonar) | Excellent for short-range (0.1 - 3m) low-cost triggers.
Note No single sensor solves perception. The art of robotics is Sensor Fusion, combining the drift-free, rich data of exteroceptive sensors with the high-speed stability of proprioceptive sensors to create a robust "Belief State" about the world.

## Slide 15: Robotic Sensors
Sensors are the primary interface between a robot and its environment.
They enable perception by converting
  Physical phenomena to electrical signals
  Electrical signals to digital data
Key Roles of Sensors
  Provide state information (position, velocity, orientation)
  Enable environment awareness (distance, obstacles, light, heat)
  Support decision-making and control

## Slide 16: Encoders
Encoders are proprioceptive sensors that measure position or rotation of joints/wheels.
Types
  Incremental encoders → measure relative motion
  Absolute encoders → provide exact position
What They Measure
  Angular position (θ)
  Velocity (by differentiation)
E.g. A mobile robot uses wheel encoders to estimate distance traveled:
  If wheel radius = r and rotation = θ
  Distance = r × θ
Used in odometry

## Slide 17: Encoder
Principle of Operation A slotted disk (code wheel) is attached to the motor shaft. An LED shines through the slots onto a photodetector. As the shaft turns, the light beam is interrupted, generating a square wave pulse train.
Quadrature Encoding: Two sensors are offset slightly. This creates two signals (Channel A and Channel B) that are 90° out of phase. By checking which channel leads, the microcontroller determines direction (forward vs. reverse).
Measurement
  Raw measurement – integer count e.g 128 ticks
  Derived measurement – angular velocity (rad/s), or linear displacement in meters
  Data type – single value (integer per channel per time step

## Slide 18: Noise and Error Characteristics
Error Type | Description | Real-World Example
Quantization Error | The smallest movement measurable is one tick. | Example: Robot moves 0.9 ticks. Sensor reports 0. Wait another millisecond, moves 0.1 tick. Sensor reports 1. Position appears to "jump" in steps.
Wheel Slip | The wheel rotates but the robot doesn't move (slipping on ice or carpet). | Fatal Odometry Error: Encoders say "Moved 10 meters forward." Reality: Robot is stuck spinning tires in a mud puddle. Odometry is optimistic.
Uneven Floor/Compression | The effective wheel radius changes due to load or soft tires. | Example: Robot carrying a heavy payload. Tires compress by 2mm. $R$ decreases. The robot travels less distance than the encoder count predicts.

## Slide 19: IMU (Inertial Measurement Unit)
An IMU is a combination of
  Accelerometer
  Gyroscope
  (sometimes) Magnetometer
What It Measures
  Linear acceleration
  Angular velocity
  Orientation (indirectly)
E.g. A drone uses IMU to maintain stability by
  Detecting tilt and adjusts motors

## Slide 20: Inertial Measurement Unit (IMU)
Principle of Operation An IMU is a fusion of three sensor types on a single silicon chip (MEMS technology).
Accelerometer
  Measures linear acceleration (including gravity vector). Works via a microscopic proof mass on a spring. When you accelerate, the mass lags, changing capacitance.
Gyroscope:
  Measures angular velocity (rad/s). Works via a vibrating mass that resists rotation (Coriolis effect).
Magnetometer:
  Measures magnetic field strength (Earth's North).
Measurement & Output:
  Raw Measurement 9-axis vector [Ax, Ay, Az, Gx, Gy, Gz, Mx, My, Mz].

## Slide 21: Inertial Measurement Unit (IMU)
Error Term | Effect | Visual Analogy
Bias Offset | Constant non-zero reading when sensor is perfectly still. | Example: Gyro reads 0.05 rad/s while sitting on a table. Integrate this for 10 seconds, robot thinks it turned 0.5 radians (~30 degrees).
White Noise | High-frequency random jitter. | You can filter this out with a Low-Pass Filter without harming the signal much.
Integration Drift | Integrating noisy gyro data to get angle results in error growing with Time t. Integrating noisy accel data to get position results in error growing with Time Squared (t2) | Example: A drone flying blind on IMU-only for 60 seconds will think it is 100 meters away from its actual location due to double integration of accelerometer noise.
Example Scenario: A robot vacuum uses a Gyroscope to maintain a straight line across the room. After 5 minutes, it has accumulated 3 degrees of drift. The previously straight stripes on the carpet become gentle curves. The robot must use a wall sensor (exteroceptive) or a floor pattern camera to "snap" its angle estimate back to reality.

## Slide 22: Ultrasonic Range Sensors (Sonar)
Ultrasonic sensors measure distance using sound waves.
Working Principle
  A speaker emits a high-frequency sound pulse (typically 40 kHz, inaudible to humans). The pulse travels at the speed of sound (approx 343 m/s), bounces off an object, and returns to a microphone. The time delay t gives distance.
  Emit sound pulse
  Measure time for echo to return
  Distance is computed using d=(v × t)/2 ​
Where:
  v = speed of sound
  t = time of flight
E.g Robot detects obstacle at 1.5 m using echo time
Limitations
Affected by:
  Soft materials (absorb sound)
  Angle of surface
Low resolution
Measurement & Output:
  Raw Measurement: Time of Flight (seconds).
  Derived Measurement: Distance (meters).
  Data Type: Single-Value (one distance per ping).

## Slide 23: Sonar Noise
Challenge | Description | Mitigation Strategy
Specular Reflection | Sound bounces off smooth surfaces like a mirror (angle of incidence = angle of reflection). If the robot is not perpendicular to the wall, the sound bounces away from the robot and never returns. | Result: Sensor reads "Max Range" (infinity). Robot thinks the path is clear and crashes into the glass wall.
Cone Angle | The sound beam is not a laser; it's a wide cone (typically 30°). | Result: The sensor reports the closest object within the cone, not necessarily straight ahead. A chair leg at 45° may trigger a "STOP" when the path directly ahead is clear.
Crosstalk | Robot A's ping is heard by Robot B. Robot B thinks it is its own echo. | Result: Robot B calculates a very short distance (Robot A is close) and jerks to a halt.
Temperature Dependence | Speed of sound v changes with air temperature. | Result: v = 331.3 + 0.606 °C. On a hot day (40°C), v is ~355 m/s. Using standard 343 m/s introduces a ~3.5% error in distance.
Sonar is cheap and reliable for short ranges but suffers from Specular Reflection and Crosstalk.

## Slide 24: Infrared (IR) Sensors
Infrared sensors use light waves to detect objects and distance.
An LED emits light (usually 850nm-950nm). A phototransistor measures the amount of reflected light.
Types
  Reflective IR (short-range detection)
  Thermal IR (heat sensing)
What They Measure
  Proximity
  Surface reflectivity
E.g. Line-following robot:
  Black line absorbs IR, resulting to low reflection
  White surface reflects IR giving high signal

## Slide 25: Infrared (IR) Sensors
Type 1: IR Proximity / Break-Beam (Intensity Based)
  Principle: Output: Non-linear analog voltage (higher voltage = closer object).
Noise/Characteristic: Highly dependent on surface color and texture.
  White wall at 10cm: High return signal -> Voltage 3.3V.
  Black velvet at 5cm: Low return signal -> Voltage 0.5V.
  Interpretation Trap: Robot sees low voltage and thinks "Object is far away." Reality: "Object is very close but black." -> CRASH.
Type 2: IR Sharp GP2Y0A Series (Triangulation Based)
  Principle: Uses a small linear CCD camera to detect the angle of the reflected IR spot, not the intensity. This is a multi-value principle internally, but outputs a single-value analog distance.
  Advantage: Surface-agnostic. Works equally well on black or white surfaces because it tracks the geometric position of the dot, not its brightness.

## Slide 26: Infrared (IR) Sensors - Measurement & Output
Data Type: Single-Value (Analog Voltage representing Distance).
Transfer Function. Extremely sensitive at close range (<10cm), very low resolution at long range (>80cm).
Common Use Case: Cliff Sensors
  Configuration: Two IR LEDs pointing down at the floor.
  Logic: If floor is present -> Strong reflection -> Robot moves forward.
  Logic: If floor is absent (Stairs) -> No reflection -> Robot Emergency Stop and Reverse.
  Noise Source: Sunlight. The sun is a massive IR emitter. IR sensors usually modulate the LED at 38kHz and filter the receiver to only listen to that frequency to ignore the DC offset of sunlight.

## Slide 27: Sensor Measurements
A sensor measurement is a numerical value representing a physical quantity.
  Encoder → angle (degrees/radians)
  IMU → acceleration (m/s²)
  Ultrasonic → distance (meters)
Measurement Process
  Physical quantity detected
  Converted to electrical signal
  Digitized into numerical value
Types of Noise
1. Random Noise
  Caused by environmental fluctuations
  E.g. small variations in IMU readings
2. Systematic Noise (Bias)
  Constant offset error
  E.g. encoder always reads +2°
3. Drift
  Error increases over time
  Common in IMUs

## Slide 28: Sensor Characteristics
1. Accuracy
  How close measurement is to true value
2. Precision
  Repeatability of measurements e.g.
  Same wrong value repeatedly → precise but not accurate
3. Resolution
  Smallest detectable change
4. Range
  Minimum and maximum measurable values
5. Sensitivity
  How much output changes with input
6. Response Time
  How quickly sensor reacts
7. Reliability - Consistency over time

## Slide 29: Single-Value vs Multi-Value Sensor Data
Single-Value Sensors
  Sensors that output one value per measurement
Examples
  Ultrasonic sensor → distance
  Temperature sensor → temperature
  IR proximity sensor → intensity
Characteristics
  Simple processing
  Low computational cost
Multi-Value Sensors
  Sensors that produce multiple data points per measurement
Examples
  Camera → image (matrix of pixels)
  LiDAR → point cloud (thousands of points)
  IMU → 3-axis acceleration + 3-axis rotation
Characteristics
  High data volume
  Requires advanced processing

## Slide 30: Comparison
Feature | Single-Value | Multi-Value
Data output | One value | Multiple values
Complexity | Low | High
Processing | Simple | Computationally intensive
Example | Ultrasonic | Camera

## Slide 31: Key Takeaways
Practical Integration Example
Autonomous Robot
Uses
  Encoders → motion tracking
  IMU → orientation
  Ultrasonic → obstacle detection
  Camera → object recognition
Combined using sensor fusion for accurate perception
Sensors convert physical world → digital data
Common sensors:
  Encoders (position)
  IMU (motion/orientation)
  Ultrasonic (distance)
  Infrared (proximity)
Measurements are affected by noise and uncertainty
Sensor quality defined by
  Accuracy, precision, resolution, range
Data types
  Single-value → simple
  Multi-value → complex but rich

## Slide 32: The Role of the Single-Value Sensor in High-Speed Loops
Why do we care so much about these "simple" single-value sensors when we have LIDAR and Cameras?
Answer: Latency and Determinism.
Multi-Value Sensors (Cameras): Processing a 1080p image to find a wall takes 20-50 milliseconds. During this time, a fast-moving drone covers 0.5 meters.
Single-Value Sensors (Encoders/IMU): Reading an encoder count takes 1 microsecond. Reading an IMU gyro takes 100 microseconds.

## Slide 33: Linking Perception to Action
In robotics, sensing alone is not useful unless it leads to action.
The key challenge is
  How can a robot respond immediately and intelligently to sensor inputs?
This leads to closed-loop control systems, where sensing continuously influences action.
A control system that continuously monitors its output (via sensors) and adjusts its input (actuators) to minimize the Error between the desired state and the current state.
Open-Loop (Feed-Forward): "I will turn my wheels for exactly 500 encoder ticks to move 1 meter." (Assumes perfect model of floor, battery voltage, and motor efficiency).
Closed-Loop (Feedback): "I want to be 1 meter away from the wall. My sensor says I am 0.8m away. Error = +0.2m. I will steer away from the wall until Error = 0."

## Slide 34: Reactive Control Loops
A reactive control loop is a system where:
  Sensor input is directly mapped to actions
  The robot responds in real-time without heavy planning
Basic Loop Structure
  Sense → Process → Act → Sense (continuous loop)
  No global map required
  Decisions are made locally and instantly
E.g. Obstacle Avoidance
  Sensor detects obstacle at 0.5 m
  Controller immediately turns robot away
No path planning needed, pure reaction

## Slide 35: Reactive Control Loops - Key Characteristics
Limitations
  No long-term planning
  Can get stuck (e.g., oscillating between obstacles)
  No global optimality
Feature | Description
Speed | Very fast response
Complexity | Low
Planning | Minimal or none
Robustness | Good in dynamic environments

## Slide 36: Feedback Control in Robotics
Reactive systems rely on feedback control.
Concept
  Measure current state
  Compare with desired state
  Adjust action to reduce error
E.g. Temperature Control
  Desired = 25°C
  Measured = 30°C
  Action = turn cooling ON
Insight - Reactive control is essentially continuous error correction.

## Slide 37: Servoing in Robotics
Servoing is the use of feedback control to achieve a desired position or state.
  The robot continuously adjusts its motion based on sensor feedback.
General Servoing Loop
  Measure current state
  Compare with desired state
  Compute error
  Apply control to reduce error
E.g. Motor Position Control
  Desired angle = 90°
  Current = 70°
  Error = 20°
  Motor rotates until error ≈ 0

## Slide 38: Visual Servoing
Visual servoing uses camera data (vision) as feedback to control robot motion.
Types of Visual Servoing
1. Image-Based Visual Servoing (IBVS)
  Control based on image features
  E.g. keep an object centered in the image
2. Position-Based Visual Servoing (PBVS)
  Uses 3D position estimation
  Requires camera calibration
Visual Servoing Loop
  Capture image
  Extract features (object position)
  Compute error (difference from desired position)
  Move robot to reduce error
E.g. Robot Arm Tracking Object
  Camera sees object slightly left
  Controller moves arm left
  Repeats until object is centered
Advantages
  High precision
  Adaptive to changes
Challenges
  Sensitive to lighting
  Requires fast image processing
  Noise in vision data

## Slide 39: World Model Approach (Deliberative Control)
A world model approach builds an internal representation of the environment and uses it for planning.
🔹 Process
  Sense environment - Fuse LIDAR, Camera, IMU -> Build Occupancy Grid Map
  Build map (world model) - localize by Use particle filter to find robot pose within the map.
  Plan actions - Run A* or RRT algorithm on the map to find global path to goal.
  Execute - Act by Execute path using a low-level PID controller
E.g. Autonomous Navigation
  Robot builds a map of a building
  Plans shortest path
  Follows planned route
Advantages
  Global optimization
  Intelligent decision-making
Limitations
  Computationally expensive to update world model
  Slow in dynamic environments
  Requires accurate models

## Slide 40: World model example
Google's Waymo (Autonomous Vehicle)
World Model: High-Definition 3D Map containing lane lines, stop sign locations, and curb heights down to the centimeter.
Action: The car follows the map precisely. It knows there is a stop sign at GPS coordinate X even if the camera is temporarily blinded by sun glare. This is the gold standard for structured environments.

## Slide 41: Behavior-Based Approach (Reactive Robotics)
A behavior-based system uses multiple simple behaviors that directly map sensing to action.
  the robot uses Behaviors, tight, hardcoded loops connecting specific sensors to specific actuators.
Examples of Behaviors
  Avoid obstacle
  Follow wall
  Move forward
How It Works
  Each behavior produces an action
  System combines behaviors
E.g. Mobile Robot
  If obstacle detected → avoid
  Else → move forward
Key Idea (Subsumption Architecture)
  Higher-priority behaviors override lower ones
  The "Obstacle Avoid" behavior can subsume (override) the output of the "Wall Follow" behavior by intercepting the motor command signalAdvantages
  Fast and robust
  Works well in dynamic environments
Limitations
  Hard to design complex behaviors
  No global planning
  Can produce unpredictable results
E.g. iRobot Roomba (Early Generations)
  No map of the room. No knowledge of where it has been.
  Behaviors: Spiral Clean, Wall Follow, Random Bounce, Cliff Avoid.
  Result: Statistically covers the floor after enough time. Incredibly robust to being picked up and moved (it doesn't care, it has no map to break).

## Slide 42: World Model vs Behavior-Based
Feature | World Model | Behavior-Based
Planning | Global | Local
Speed | Slow | Fast
Complexity | High | Moderate
Adaptability | Low in dynamic environments | High
Example | Path planning robot Navigation: Finding the shortest path. | Obstacle avoidance robot Survival: Not hitting things, balancing.
Core Philosophy | Representation, Reasoning | Situatedness, Embodiment
Reaction Time | ~100ms - 1s+ | ~1ms - 100ms

## Slide 43: Hybrid Approach (Modern Systems)
Combines:
  Deliberative planning (world model)
  Reactive control (behaviors)
E.g. Self-Driving Car
  Global planner → route to destination
  Reactive system → avoid pedestrians
Integrated Example
Warehouse Robot
  Reactive Layer - Avoid obstacles
  Servoing - Align with shelf using vision
  World Model - Plan route to storage location
All systems work together

## Slide 44: Hybrid Approach (Modern Systems)
Layer | Type | Function | Cycle Time | Example Tech
Deliberative | World Model | Global Planning, Localization, Task Allocation | Minutes / Seconds | SLAM Graph Optimization
Sequencing | Hybrid | Executing the plan step-by-step (e.g., "Go through door") | Seconds | State Machine (SMACH)
Reactive | Behavior-Based | Collision avoidance, motor control, visual servoing | Milliseconds | PID, IBVS, Obstacle Stop
Modern mobile robots do not choose between World Model and Behavior-Based; they layer them. This is often called a Three-Layer Architecture. Example Scenario: Robot Waiter Delivering Coffee
Deliberative Layer (Slow): Thinks: "Table 4 is at coordinates (12.3, 5.1). I will plan a global path via the main aisle."
Sequencing Layer (Medium): Monitors: "I have reached the waypoint near the aisle. Behavior Switch: Activate 'Visual Servoing' to align tray with table edge marker."
Reactive Layer (Fast): Senses: "Proximity sensor spike on the right! A child just ran by." Action: Emergency stop. After child passes: Resume.

## Slide 45: Takeaways
Reactive control loops enable fast, real-time response
Servoing ensures precise control using feedback
Visual servoing uses camera data for control
World model approach enables global planning
Behavior-based approach enables fast reactions
Modern robots use hybrid architectures

## Slide 46: Exam-Oriented Questions
Define reactive control loop with example
Explain visual servoing and its types
Compare world model and behavior-based approaches
Discuss advantages of reactive control systems
Explain how servoing improves robot accuracy