## Slide 1: Localization and Navigation

## Slide 2: Localization
Localization is the process by which a robot determines its position and orientation (pose) within an environment using sensor data and a given map.
Pose is typically represented as (x, y, θ)
where
  x, y represents position in space
  Θ represents orientation (heading angle)
Why Localization Matters
A robot cannot navigate effectively unless it knows
  Where it is
  Where it is going
  How to get there
Localization vs. Navigation
Localization. Knowing where you are.
Navigation. The combination of localization, path planning, and control to get from point A to point B.

## Slide 3: Types of localization
Local Localization – Robot knows its approximate starting position
Global Localization – Robot has no idea where it is initially
Kidnapped Robot Problem – Robot is suddenly moved to an unknown location

## Slide 4: Types of Localization
Type | Description | Analogy
Position Tracking | Initial pose known; track changes over time. Most common. | Driving with a GPS that occasionally loses signal but knows where you started.
Global Localization | Initial pose unknown; robot must determine where it is from scratch. | Waking up in a hotel room with no idea which city you're in.
Kidnapped Robot Problem | Robot is secretly moved without its knowledge; must re-localize. | You close your eyes, someone spins you around and moves you, now find the door.

## Slide 5: The Challenge of Uncertainty
Real-world robotics operates under uncertainty, due to imperfect sensors and actuators.
Sources of Uncertainty
Sensor Noise
  GPS inaccuracies
  Noisy camera or LiDAR readings. E.g. LiDR returns 5.0 meters to a wall, but the true distance is 5.02 m
Actuator Noise
  Wheels slip
  Motors don’t move exact distances
  Friction, surface texture, motor heating, all introduce errors.
  E.g. A differential drive robot commanded to turn 90° might turn 87° on carpet, 91° on tile.
3. Environmental Uncertainty
  Dynamic obstacles (people, cars)
  Changing environments
  Perceptual Aliasing - Different locations look identical to the robot's sensors
E.g. A robot is commanded to move 1 meter forward, but
  It actually moves 0.95 m or 1.05 m
  Over time, small errors accumulate → drift
Insight: Localization is not about exact position, it is about probability.

## Slide 6: Belief Representation - Where is the Robot?
Because of uncertainty, robots represent their position as a belief,
  a probability distribution over possible locations.
A belief is
  Bel(x) = P(robot is at position x)
Types of Belief Representations
1. Discrete Representation
  Environment divided into cells
  Each cell has a probability
  E.g.
  Robot is most likely in Cell B
2. Continuous Representation
Uses probability density functions (e.g., Gaussian). E.g.
  Mean = estimated position
  Variance = uncertainty
Cell | Probability
A | 0.1
B | 0.6
C | 0.3

## Slide 7: The Probabilistic Solution
We don't ask "Where is the robot?"
We ask: "What is the probability distribution over all possible poses?"
Belief bel(x_t) = P(x_t | z_{1:t}, u_{1:t})
  x_t = robot state (pose) at time t
  z_{1:t} = all sensor measurements from time 1 to t
  u_{1:t} = all control commands from time 1 to t
This is a conditional probability.
  The probability of being at x_t given everything we have seen and done.

## Slide 8: Bayesian Update (Core Idea)
Localization uses a cycle
  Prediction (Motion Update)
  Correction (Sensor Update)
Bel(xt) = η P(zt ∣ xt) ∫ P(xt ∣ xt−1, ut) Bel(xt−1) dxt−1
Where:
  Bel (xt) is updated belief
  P (zt ∣ xt) is sensor model
  P (xt ∣ xt−1, ut) is the motion model
  η is the normalization constant

## Slide 9: Bayesian Update (Core Idea)
E.g.
  Robot thinks it's near a door (prediction)
  Sensor detects a wall instead, then belief shifts
Common Localization Algorithms
  Kalman Filter (linear systems)
  Extended Kalman Filter (EKF) (nonlinear)
  Particle Filter (non-parametric, widely used)

## Slide 10: Belief Representation - "Where is the Robot?"
How do we store and update this probability distribution in memory?
Three common approaches
A. Parametric (Gaussian / Kalman Filter)
Idea: Represent belief as a single peak (mean) with an uncertainty (covariance).
Shape: Unimodal (one "best guess").
Good for: Position tracking when uncertainty is small.
Bad for: Global localization (multiple possible poses).
Example Belief: x = 5.2m, σ² = 0.1m² → "I'm 95% confident I'm between 5.0m and 5.4m"

## Slide 11: Non-Parametric - Histogram / Discrete Bayes
Idea. Discretize the world into bins. Each bin has a probability.
Shape. Can represent multiple hypotheses (multimodal).
Memory. O(N) where N = number of bins. World gets large quickly.
Example: Corridor of 20m, discretized into 1m bins. Bin 0: 0.01, Bin 1: 0.01, ..., Bin 7: 0.70, Bin 8: 0.25, Bin 9: 0.01... → "I'm probably at 7m, possibly at 8m, not elsewhere"

## Slide 12: Non-Parametric - Particle Filter (Monte Carlo Localization - MCL)
Idea. Represent belief as a set of random samples ("particles"). Each particle is a hypothesis.
Shape. Highly flexible, any distribution.
Popular because. Efficient, handles ambiguity well, easy to implement.
Example: 100 particles.47 particles at x=7m, 38 at x=8m, 10 at x=12m, 5 elsewhere.→ "Strong belief in two places (7m and 8m), weak third hypothesis at 12m"

## Slide 13: Map Representation - Occupancy Grids
An occupancy grid divides the environment into a grid of cells where each cell stores the probability of being occupied.
Each cell has a value
  0 → Free space
  1 → Occupied
  0.5 → Unknown
Example Grid
  [0.1, 0.2, 0.9] [0.0, 0.8, 0.7] [0.0, 0.1, 0.2]
High values → obstacles
Low values → free space
Visualization
  Dark cells → obstacles
  Light cells → free space
Updating Occupancy Grids
Sensor readings update the probability of each cell:
  Laser scan detects obstacle → increase occupancy probability
  No obstacle detected → decrease probability

## Slide 14: Map Representation - Occupancy Grids
We have a belief. But what map are we localizing against? The classic answer: Occupancy Grid Maps.
The Core Idea
Discretize the world into a grid of cells. Each cell stores the probability that it is occupied.
How to Update an Occupancy Grid (Log-Odds Form)
  We don't store raw probabilities (too numerically unstable). We store log-odds
  l(x,y) = log( P(x,y) / (1 - P(x,y)) )
Update rule (simple version)
  l_new=l_old+log(p_meas/(1-p_meas)) - log( p_prior/(1-p_prior))
  Where p_meas is the sensor's model (e.g., "LiDAR returns occupied with probability 0.9 if cell is truly occupied").
Intuition: Each sensor reading adds evidence for or against occupancy.

## Slide 15: Mathematical Update Rule
Advantages of Occupancy Grids
  Simple and intuitive
  Works well with sensor fusion
  Suitable for unknown environments
Limitations
  Memory intensive for large environments
  Resolution trade-off
    High resolution → accurate but slow
    Low resolution → fast but less precise

## Slide 16: Localization on an Occupancy Grid
The robot's localization algorithm (e.g., Particle Filter) uses the occupancy grid as the reference map.
How a particle gets a "weight" (importance) during localization
For each particle with pose (x, y, θ):
  Project the robot's expected sensor readings using the occupancy grid.
  Compare to actual sensor readings.
  Weight = similarity (e.g., number of matching occupied cells).
Particles that agree with the map get high weight. Particles that suggest the robot is inside a wall get low weight (and are eventually discarded).

## Slide 17: Complete Localization Loop
Initialize: 1000 particles uniformly across free space (from occupancy grid) Repeat every 50ms
Motion prediction - Move each particle according to odometry + noise
Sensor update - Weight particles by how well their expected scan matches actual scan (using grid)
Resample - Draw new particles proportional to weights (low weight particles die)
Estimate pose - Weighted average of all particles
Update occupancy grid - Add new free/occupied evidence to map (if building map online)

## Slide 18: Linking Localization & Navigation
Localization and mapping work together
Component | Role
Localization | Where am I?
Mapping | What does the world look like?
Navigation | How do I move safely?
SLAM (Simultaneous Localization and Mapping)
When the robot
Does not know the map
Must build the map and localize simultaneously
Example Scenario - A robot vacuum
Builds a map of your house (occupancy grid)
Tracks its position (localization)
Plans cleaning paths (navigation)

## Slide 19: Practical Example: Mobile Robot in a Corridor
Initial Belief - Robot uncertain → spread across multiple positions
Movement - Moves forward → belief shifts
Sensor Reading - Detects door → probabilities updated
Convergence - Belief becomes concentrated → robot localized

## Slide 20: Key Takeaways
Localization is about estimating position under uncertainty
Robots use probability distributions (beliefs) instead of exact positions
Bayesian filtering is the foundation of localization
Occupancy grids provide a practical way to represent maps
Localization + Mapping = SLAM, a core robotics problem

## Slide 21: Take away
Concept | Key Takeaway | Example
Localization | Estimating pose relative to a map | "I am at x=3.2m, y=1.5m, facing north"
Uncertainty | Belief is a probability distribution | 70% at 3m, 30% at 8m (perceptual aliasing)
Belief Representation | Gaussian, Histogram, or Particles | Particle filter: 500 hypotheses
Occupancy Grid | Map as probability per grid cell | 0.9 = wall, 0.1 = free, 0.5 = unknown